## Slide 1: MRE 492 Robotic Vision
Representing Position and Orientation

## Slide 2: Outline
Position and Orientation
Representing Poses in 2D
Representing Poses in 3D
  Rotation Matrices
  Three-angles
  Axis-angles
  Unit Quaternions
  3D Poses

## Slide 3: Positions and Orientations
Need for representing positions and orientations in space.
The position of a point is represented by a vector of coordinates.

## Slide 4: Representing a set of points
Method 1: Represent the position and orientation of each point separately
Method 2: Represent the points in the set’s reference frame and represent the position and orientation of that frame (with ξB ).

## Slide 5: Representing a set of points
Notes: Each model have a “reference” frame location

## Slide 6: Investigating pose in 2D
𝑦𝐴
𝐵
𝐴𝜉𝐵
𝐴 𝑥𝐴
Recall that we can think of 𝐴𝜉𝐵 as the translation and rotation required in order to make
𝐴 coincide with 𝐵
𝑥𝐵
𝑦𝐵
𝑃

## Slide 7: Investigating pose in 2D
𝑦𝐴
𝐴𝒕𝐵
𝐴 𝑥𝐴
Recall that we can think of 𝐴𝜉𝐵 as the translation and rotation required in order to make
𝐴 coincide with 𝐵
To coincide with 𝐵 , 𝐴 must undergo a translation 𝐴𝒕𝐵 and a rotation by an angle 𝜃
𝐵
𝑥𝐵
𝑦𝐵
𝑃


## Slide 8: Investigating pose in 2D
Let 𝐴𝒑 =
𝐴𝑥, 𝐴𝑦 𝑻, 𝐵𝒑 =
𝐵
𝐵𝑥, 𝐵𝑦 𝑻 and 𝐴𝒕 =
𝐵x
𝐴𝑡
𝐵y
, 𝐴𝑡
𝑻
𝐴𝒕𝐵
𝑥𝐴
𝑦𝐴
𝐴
𝐵
𝑥𝐵
𝑦𝐵
𝑃
𝐴𝑥
𝐴𝑡𝐵x
𝐴𝑦
𝐴𝑡𝐵y
𝐵𝑦
𝐵𝑥


## Slide 9: Investigating pose in 2D
Let 𝐴𝒑 =
𝐴𝑥, 𝐴𝑦 𝑻, 𝐵𝒑 =
𝐵
𝐵𝑥, 𝐵𝑦 𝑻 and 𝐴𝒕 =
𝐵x
𝐴𝑡
𝐵y
, 𝐴𝑡
𝑻
𝐴𝒕𝐵
𝑥𝐴
𝑦𝐴
𝐴
𝐵
𝑥𝐵
𝑦𝐵
𝑃
𝐴𝑥
𝐴𝑡𝐵x
𝐴𝑦
𝐴𝑡𝐵y
𝐵𝑦
𝐵𝑥

From the figure we can see that
A x  At  B x cos  B y sin
Bx
A y  At  B x sin  B y cos
By
𝐵𝑦
𝐵𝑥


B x cos
B y sin
B x cos
B y sin

## Slide 10: Investigating pose in 2D

## Slide 11: Investigating pose in 2D
Can we represent the pose 𝐴𝜉𝐵 by the pair
𝐴𝑅𝐵, 𝐴𝒕𝐵 ?

## Slide 12: Investigating pose in 2D
Can we represent the pose 𝐴𝜉𝐵 by the pair
𝐴𝑅𝐵, 𝐴𝒕𝐵 ?
Yes, but there is a better option!
Notes: Change from non-linear operation to linear

## Slide 13: Investigating pose in 2D
Observe the following equivalence
Can we represent the pose 𝐴𝜉𝐵 by the matrix 𝐴𝑇𝐵?
Yes, and the algebraic properties are nice!

## Slide 14: Investigating pose in 2D
But…
We are describing points in the plane with 3 coordinates despite that they only have 2 degrees of freedom…
The non linear transformation 𝐵𝒑 ↦ 𝐴𝒑 then becomes a linear transformation 𝐵𝒑 ↦ 𝐴𝒑
What is going on?

## Slide 15: Investigating pose in 2D
We have “discovered” some basic constructions from projective geometry

## Slide 16: Investigating pose in 2D
We have “discovered” some basic constructions from projective geometry
Linear transformation
of the projective plane 2
Non-linear transformation of the Euclidean plane ℝ2
Points in the Euclidean plane are described by Cartesian coordinates
Points in the projective plane are described by homogeneous coordinates
This means that they are only unique up to scale, i.e.
𝑥, 𝑦, 1 = 𝜆𝑥, 𝜆𝑦, 𝜆 ∀ 𝜆 ∈ ℝ\ 0
The matrix representing the projective transformation is also homogeneous, i.e.
𝐴𝑇𝐵 = 𝜆𝐴𝑇𝐵∀ 𝜆 ∈ ℝ\ 0 37

## Slide 17: Investigating pose in 2D
Many problems in computer vision are easier to express and solve if we choose to think of points and transformations in terms of projective geometry
– Algebra and computations become simpler
Notes: Matrix can be treated as a way of projection from one vector space to another

## Slide 18: Representing pose in 2D

## Slide 19: Example
𝑥𝐴
Let 𝐴𝒕𝐵 = 4,1 𝑇, 𝐵𝒑 = 2,3 𝑇 and 𝜃 = 27°
Determine the pose of of 𝐵 relative to 𝐴 , i.e. 𝐴𝑇𝐵
Determine the coordinates of 𝑃 in 𝐴 , i.e. 𝐴𝒑
𝑦𝐴
𝑥𝐵
𝜃
𝑃
𝑦𝐵
𝐵𝒑
𝐴𝒑
𝐴𝒕𝐵

## Slide 20: Example
From the previous slides we know that
This allows us to compute 𝐴𝒑
This can also be verified by drawing

## Slide 21: Example
𝑥𝐴
𝑦
𝐴
𝑥𝐵
𝑦𝐵
27°
𝑃
1
3
2
4.5810
2
3
4
1
2
3
4 4.4200
𝐴𝒕𝐵

## Slide 22: General properties
𝐴 coincide
Let us denote by 𝐴𝜉𝐵 the pose of frame 𝐵 relative to frame 𝐴
We can think of 𝐴𝜉𝐵 as the translation and rotation required in order to make with 𝐵
𝑥𝐴
𝑦𝐴
𝐴
𝑥𝐵
𝐵
𝐴𝜉𝐵
𝑦𝐵

## Slide 23: General properties
A point 𝑃 can be described with respect to either frame
These descriptions are related by the pose
Formally we write this as 𝐴𝒑 = 𝐴𝜉𝐵 ∙ 𝐵𝒑
𝑥
𝐴
𝑦𝐴
𝐴
𝐵
𝑥𝐵
𝑦𝐵
𝐴𝜉𝐵
𝑃
𝐴𝒑
𝐵𝒑
Note that 𝐴𝒑 and 𝐵𝒑 are different vectors!!!

## Slide 24: General properties
Action on points
𝐴𝒑 = 𝐴𝜉𝐵 ∙ 𝐵𝒑
Composition
𝐶
𝐴𝜉
= 𝐴𝜉𝐵⨁𝐵𝜉𝐶
𝑥𝐴
𝑦
𝐴
𝐴
𝐵
𝑥
𝐵
𝑦𝐵
𝐵
𝐴𝜉
𝐶
𝐵𝜉𝐶
𝑥𝐶
𝑦𝐶
𝐶
𝐴𝜉
𝑥𝐴
𝑦𝐴
𝐴
𝐵
𝑥𝐵
𝑦
𝐵
𝐴𝜉𝐵
𝐴𝒑
𝐵𝒑
𝑃
What about 𝐴𝜉𝐵⨁𝐵𝜉𝐴?

## Slide 25: General properties
Action on points
𝐴𝒑 = 𝐴𝜉𝐵 ∙ 𝐵𝒑
Composition
𝐴𝜉𝐶 = 𝐴𝜉𝐵⨁𝐵𝜉𝐶
Inverse
⊖ 𝐴𝜉𝐵 = 𝐵𝜉𝐴
Neutral element
0 = 𝐴𝜉𝐴
0 ⊕ 𝜉 = 𝜉
𝜉 ⊖ 0 = 𝜉
𝜉 ⊖ 𝜉 = 0
⊖ 𝜉 ⊕ 𝜉 = 0
𝑥𝐴
𝑦
𝐴
𝐴
𝐵
𝑥
𝐵
𝑦𝐵
⊖ 𝐴𝜉𝐵
𝑥𝐴
𝑦
𝐴
𝐴
𝐵
𝑥
𝐵
𝑦𝐵
𝐵
𝐴𝜉
𝐶
𝐵𝜉𝐶
𝑥𝐶
𝑦𝐶
𝐶
𝐴𝜉
𝑥𝐴
𝑦𝐴
𝐴
𝐵
𝑥𝐵
𝑦
𝐵
𝐴𝜉𝐵
𝐴𝒑
𝐵𝒑
𝑃

## Slide 26: Example
Vehicle
Point observed by the camera
𝑃
𝑊
𝑉
Camera
𝐶
World

## Slide 27: Example
𝐶𝒑
Camera
𝐶
Point observed by the camera
𝑃
𝑉𝜉𝐶
𝑊
𝑊𝜉𝑉
𝑉
World
Vehicle

## Slide 28: Example
𝐶
Point observed by the camera
𝑃
Camera
𝒑
𝐶
𝑊𝜉𝐶 = 𝑊𝜉𝑉⨁𝑉𝜉𝐶
𝑉𝜉𝐶
𝑊
𝑊𝜉𝑉
𝑉
World
Vehicle
𝑊𝜉𝐶

## Slide 29: Example
𝐶
Point with a known position relative to the camera
𝑃
Camera
𝒑
𝐶
𝑉𝒑
𝑉𝒑 = 𝑉𝜉𝐶 ∙ 𝐶𝒑
𝑊𝜉𝐶 = 𝑊𝜉𝑉⨁𝑉𝜉𝐶
𝑊𝜉𝐶
𝑉𝜉𝐶
𝑊
𝑊𝜉𝑉
𝑉
World
Vehicle

## Slide 30: Example
𝐶
Camera
Point with a known position relative to the camera
𝑃
𝒑
𝐶
𝑉𝒑
𝑉𝒑 = 𝑉𝜉𝐶 ∙ 𝐶𝒑
𝑊𝒑
𝑊𝒑 = 𝑊𝜉𝑉⨁𝑉𝜉𝐶 ∙ 𝐶𝒑
𝑊𝜉𝐶 = 𝑊𝜉𝑉⨁𝑉𝜉𝐶
𝑊𝜉𝐶
𝑉𝜉𝐶
𝑊
𝑊𝜉𝑉
𝑉
World
Vehicle

## Slide 31: Pose Graph

## Slide 32: Example

## Slide 33: Representing 3D Orientations with Rotation Matrices
3D rotations around the origin of R3 form the rotation group.
3D rotations can be uniquely parametrized by special orthogonal matrices (rotation matrices).
Compounding still holds: C RA = C RBB RA.
Rows of a rotation matrix give the directions of the new frame’s axes relative to the current frame.
More parameters than degrees of freedom.
The rotation group is often referred to as the special orthogonal group
SO(3).

## Slide 34: Representing pose in 3D

## Slide 37: Roll-Pitch-Yaw Convention
Roll , Pitch , Yaw
Conversion to 3x3 rotation matrix:
Notes: Rotate along x first, then y and z
Try MATLAB Code:
R = rotz(0.1) * roty(0.2) * rotz(0.3);
R = eul2r(0.1, 0.2, 0.3)
gamma = tr2eul(R)
R = eul2r(0.1 , -0.2, 0.3)
tr2eul(R)
eul2r(ans)
R = eul2r(0.1, 0, 0.3)
tr2eul(R)

## Slide 38: Representing 3D Orientations with Three Angles
Given three angles (α, β, γ), let a-b -c denote the application of
a rotation of α around axis a,
a rotation of β around axis b , b is b rotated by α around a
and a rotation of γ around axis c (in that order), c is c rotated by α around a, then by β around b
x', x''
x
y
z, z'
z'', z'''
x'''
y'''
α
β
γ
Three angles (α, β, γ), 12 representations of a 3D rotation:
Euler angles: z-x -z , x-y -x , y-z -y , z-y -z , x-z -x , y-x -y .
Tait–Bryan angles: x-y -z , y-z -x , z-x -y , x-z -y , z-y -x , y-x -z .
This is called the three-angle representation with intrinsic rotations.
Notes: Note: Intrinsic vs Extrinsic Rotations
Intrinsic rotations apply to axis in rotated coordinate system
Coordinate system of next rotation relative to previous rotation
Extrinsic rotations apply to axis in world coordinate system
Coordinate system of next rotation relative to (fixed) world coordinate system

## Slide 39: Representing 3D Orientations with Three Angles
Three-angle representation with extrinsic rotations
Given three angles (α, β, γ), let a-b-c denote the application of
a rotation of α around axis a,
a rotation of β around axis b,
and a rotation of γ around axis c (in that order).
Three angles (α, β, γ), another 12 representations of a 3D rotation:
Euler angles: z-x-z, x-y-x, y-z-y, z-y-z, x-z-x, y-x-y.
Tait–Bryan angles: x-y-z, y-z-x, z-x-y, x-z-y, z-y-x, y-x-z.
This is called the three-angle representation with extrinsic rotations.

## Slide 40: Visualizing Intrinsic Three-angles
x', x''
x
α
Example: Given three angles (α, β, γ), z-x -z denotes the application of
a rotation of α around axis z,
a rotation of β around axis x , x is x rotated by α around z
and a rotation of γ around axis z (in that order),
z is z rotated by α around z, then by β around x
z, z'
y'''
z'', z'''
β
y
x'''
γ

## Slide 41: Three-angles: Matrix Equivalents
Intrinsic rotations equivalent with rotation matrices:
x-y -z : Rx(α)Ry (β)Rz (γ)
z-x -z : Rz (α)Rx(β)Rz (γ)
Compare with:
Extrinsic rotations equivalent with rotation matrices:
x-y-z: Rz (γ)Ry (β)Rx(α)
z-x-z: Rz (γ)Rx(β)Rz (α)

## Slide 42: There Are 24 Three-angles Representations
Extrinsic Euler: z-x-z, x-y-x, y-z-y, z-y-z, x-z-x, y-x-y.
Intrinsic Euler: z-xI-zII, x-yI-xII, y-zI-yII, z-yI-zII, x-zI-xII, y-xI-yII. Extrinsic Tait-Bryan: x-y-z, y-z-x, z-x-y, x-z-y, z-y-x, y-x-z.
Intrinsic Tait-Bryan: x-yI-zII, y-zI-xII, z-xI-yII, x-zI-yII, z-yI-xII, y-xI-zII.
When you read a book, or code documentations, you almost never know if the author is using intrinsic or extrinsic ( and are omitted). The Corke book doesn’t say it’s using intrinsic rotations.
Often, you will not know which of the Euler or TB representation the author is using.
With TB representations, some authors give the three angles in inverse order (i.e., in the order of the rotation matrix form).
All of the above are the first reason why three-angles are horrible.

## Slide 43: Why Three-angles Are Horrible
24 representations, plus different names (TB also called yaw-pitch-roll, TB sometimes referred to as Euler).
Singularities: Assuming Euler z-y -z ,
(α, 0, γ) ∼ (α + c, 0, γ − c)∀c ∈ R
Numerical instability.
Three-angle representations are horrible. You should avoid using them.
However, you will come across them outside of this class. Thus you must know how to read them.

## Slide 44: Representing Rotations with Axis-angles
Any 3D rotation can be expressed as a rotation of θ around an axis v.
This is an intuitive representation, but compositions are not as easy as with rotation matrices.

## Slide 45: Conversion
Rodriguez’ formula
Inverse

## Slide 46: Quaternions: History & Definition

## Slide 47: Quaternion Arithmetic: Sum, Product

## Slide 48: Quaternion Arithmetic: Product

## Slide 49: Quaternion Arithmetic: Conjugate, Absolute value, Inverse

## Slide 50: Representing 3D Rotations with Unit Quaternions

## Slide 51: Unit quaternions for a 3D rotation

## Slide 52: Distance Between Two Rotations

## Slide 53: Benefits of Unit Quaternions for Representing 3D Rotations
Not even speaking about three-angles. Axis-angles are awkward to compose.
Compared to rotation matrices:
Compact representation;
More efficient for composition;
Intuitive metric;
Smooth interpolation;
Robustness to numerical drift

## Slide 54: Representing 3D transformation/poses with 3-vectors and Quaternions

## Slide 55: Representing pose in 3D